Add header on biniary file with
ID of the digitizer
Data structure (in Setup directory?)
Run number
Structure of the data director with separate subdirectory fot tracker, PID, gamma e setup
The macro that convert binary to root file take the link between digitizer and anode section from separate configuration file. The macro should provide for different level of
min level all the original data are kept to havemaximum flexibility during test.
max level only the usefull data are kept and all the other are not copied to save space
Separation of the flag variable in two different variable (to be alligned with the digitizers documentation)
RUN XX
tracker
PID
gamma
Setup

---
Assunto come riferimento il fascio la x cresce da dx verso sx
Sistema di riferimento come quello del FPD
Everything start from 0

---
DEFINITIONS
- Hit: All the information relate to the signal in a single pad
  entry is related to the organization of this information on a root or binry file, hit is the corresponding physical phenomeno
- Event: It is the totality of hit generated by a single physical event (e.g.
  charged particle crossing the detector)
- Cluster: Group of entries that are close in space and time (not necessarely
  part of a physical event)
- Row: is the totality of pad or strip tha have same z-coordinate (in the final	detector a row is made or of 64x). It is divided in four segments corresponding to the four sections of the anode.
- Strip: Is the sensible area of the anode between two rows. Each strip is made of four long segment (300 mm) each one corresponding to a section of the anode.
  Inside the code strip and row are both called row. The proper raw have an index that run from 0 to 4 and 60x4 pads, the strips instead have an index between 5 and 10 and just 4 pads.

---
strip segment (pad inside the software)
pad
Top View / External view
3
2
4
3
2
1
0
3
2
4
3
2
1
0
3
2
4
3
2
1
0
3
2
4
3
2
1
0
3
2
4
3
2
1
0
3
2
Strip (row inside software)
row
239
239
239
239
180
181
182
183
184
183
183
180
181
182
183
184
183
183
180
181
182
183
184
183
183
180
181
182
183
184
183
183
180
181
182
183
184
183
183
239
179
179
179
179
179

---
19
18
17
16
15
14
13
12
11
10
9
8
7
6
5
4
Section number
3
2
1
0
      Column 3	Column2	Column 1	Column 0
Bottom view (internal view).
Full anode (group of all 4 anodes)
Single anode (single anodic board corresponding to a column)
Anode section (group of pad and strip linked to a digitizer)
   At each anode section is linked one and only one digitizer and a preamplifier
Anode section row column	ID dig ID preampl
0	0	0	xxx	yyyy
1	0	1	xxy	yyyx
2	0	2	…	...
3	0	3	…	...
4	1	0	…	...
5	1	1	…	...
6	1	2	…	...
19	4	3
Template for the anode map file.
beam

---
Software nomenclature
Top view / External view of a single anodic board
row
row
10
59
4
3
2
1
0
4
9
59
4
3
2
1
0
3
8
59
4
3
2
1
0
2
7
59
4
3
2
1
0
1
6
59
4
3
2
1
0
0
5
beam

---
Electronics nomenclature
Top view / external view of a single anodic board
strip
row
Pl6
1
2
3
59
60
E
Pl5
1
2
3
59
60
D
Pl4
1
2
3
59
60
C
Pl3
1
2
3
59
60
B
Pl2
1
2
3
59
60
A
Pl1
beam

---
Electronics nomenclature
Bottom view / internal view of a single anodic board
row
E
D
C
B
A
60 59 58	4 3 2 1
beam

---
JA
JB
JC
JD
JE
Connector	channels elec. nom. Channel software nom.
JA	row A + Pl1	row 0 + row 5
JB	row B + Pl2	row 1 + row 6
JC	row C + Pl3	row 2 + row 7
JD	row D + Pl4	row 3 + row 8
JE	row E + Pl5 + Pl6	row 4 + row 9 + row 10

---
Top view / External view of the full anode with an highlight (red) on a single section of the anode
3
2
1
0
239
0
3
2
1
0
239
0
3
2
1
0
239
0
3
2
1
0
239
0
3
2
1
0
239
179
119
65
64
63
62
61
60
59
5
4
3
2
1
0
3
2
1
0

---
92.80
The active area of the detector start from +2 mm
beam

---
Raw	centre	Close edge	Far / edge	width
5	7.75	2	13.5	11.5
0	18.60	13.5	23.7	10.2
6	29.20	23.7	34.7	11
1	39.8	34.7	44.9	10.2
7	50.4	44.9	55.9	11
2	61	55.9	66.1	10.2
8	71.6	66.1	77.1	11
3	82.20	77.1	87.3	10.2
9	92.80	87.3	98.3	11
4	103.4	98.3	108.5	10.2
10	114.25	108.5	120.0	11.5
Depth 128 mm
Metal-coated depth 118
The insulation layer between the raws has been neglected!

---
Adpater Samtec flat – 64 Ch ERF8
In adapter	Out preamp
48	40
49	56
50	41
51	57
52	42
53	58
54	43
55	59
56	44
57	60
58	45
59	61
60	46
61	62
62	47
63	63
In adapter	Out preamp
32	32
33	48
34	33
35	49
36	34
37	50
38	35
39	51
40	36
41	52
42	37
43	53
44	38
45	54
46	39
47	55
In adapter	Out preamp
0	0
1	16
2	1
3	17
4	2
5	18
6	3
7	19
8	4
9	20
10	5
11	21
12	6
13	22
14	7
15	23
In adpter	Out preamp
16	8
17	24
18	9
19	25
20	10
21	26
22	11
23	27
24	12
25	28
26	13
27	29
28	14
29	30
30	15
31	31

---
Pinout of different elements
Pin number SAMTEC	| channel PA
ERF8
1	|	bias 0:31
2	|	bias 0:31
3	|	N.C
4	|	N.C
5	|	16
6	|	0
7	|	17
8	|	1
9	|	18
10	|	2
⁞	⁞
33	|	30
34	|	14
35	|	31
36	|	15
37	|	N.C.
38	|	N.C.
39	|	GND
40	|	GND
41	|	GND
42	|	GND
43	|	N.C.
44	|	N.C.
45	|	48
46	|	32
47	|	49
48	|	33
49	|	50
50	|	34
⁞	⁞
71	|	61
72	|	45
73	|	62
74	|	46
75	|	63
76	|	47
77	|	N.C.
78	|	N.C.
79	|	bias 32:63
80	|	bias 32:63
Pad number	| output channel PA
0	|	1
1	|	2
2	|	3
3	|	4
⁞	|	⁞
59	|	60
Strip	|	61
Strip2	|	62 (if row is 4)
ERF8

---
Pinout of different elements
Pin number SAMTEC	| out channel in flat cable
ERF8
1	|	N.C.
2	|	N.C.
3	|	N.C.
4	|	N.C.
5	|	16
6	|	0
7	|	17
8	|	1
9	|	18
10	|	2
⁞	⁞
33	|	30
34	|	14
35	|	31
36	|	15
37	|	N.C.
38	|	N.C.
39	|	N.C.
40	|	N.C.
41	|	N.C.
42	|	N.C.
43	|	N.C.
44	|	N.C.
45	|	48
46	|	32
47	|	49
48	|	33
49	|	50
50	|	34
⁞	⁞
71	|	61
72	|	45
73	|	62
74	|	46
75	|	63
76	|	47
77	|	N.C.
78	|	N.C.
79	|	N.C.
80	|	N.C.
SAMTEC to Flat converter (by Fabio L.)
ERF8

---
 First pin in SAMTEC connectors and cables
ERF8
ERCD

---
Electrical connection between Bias supply and Tracker

---
1
1
2
3
4
a
t3
b1
b2
b3
t3
b3
b2
b1
c
Top view anode
CAEN A1015G
Connectors
Flange
GND
1
0
Anode (if unsegmented anode) or not connected
1
1
gnd
0
1
2
3
4
5
Top 3
2
top2/bot3
3
A
b3
b1
C
t3
b2
top1/bot2
4
bot1
5
Not connected
6
Detector
7
catode

---
Angles
Lab frame
z
θ
αl is positive
θl is positive
αl+θl=90
α
0
x
1200
y
Analisis frame
θ
αA is negative
θA is negative
αA+θA=-90
α
0
1200
x

---
Angles
y
Analisis frame
θ
αl is negative
θl is negative
αl+θl = -90
α
0
x
5 points: (xi , yi) i=0,4;
Fit y = a+ bx
αl = atan(b)
θl = -90 -αl
θA = -θl = 90 + αl
Since we actually need acotan(b) instead of atan(b) we define θl in the followinf way
theta_deg=-90-alpha_deg;
   if(theta_deg<-90){
      theta_deg=-90-alpha_deg+180;
   }

---
Angles
y
0
x
theta_deg=-90-alpha_deg;
theta_deg=-90-alpha_deg;
   if(theta_deg<-90){theta_deg=-90-alpha_deg+180;}